## Slide 1
mmWave Radar for Live Animal Detection
in Passenger Screening
Enhancing Biosecurity at Clearance Checkpoints with Advanced Radar Sensing
July 2026
1 / 16

## Slide 2
Problem Statement
Illegal animal importation screening
2 / 16
Government seeking advanced technology to enhance passenger screening at clearance halls
Assist frontline officers in identifying and intercepting illegal animal importation
Animals concealed within baggage, backpacks, or luggage
Quick and accurate detection of live animals required
Focus on warm-blooded animals — cold-blooded detection highly preferred
💡 Goal: A system that detects live animals through baggage non-invasively, with high throughput and no ionizing radiation.

## Slide 3
Why mmWave Radar?
Core technology differentiators
3 / 16
Electromagnetic waves penetrate non-metallic materials
→ Clothing, backpacks, plastic containers, cardboard
MIMO radar creates high-resolution 3D images
Key advantage: 3D Doppler Imaging
Detects micro-movements even when animal is still:
→ Breathing (~0.1–3 Hz, 0.1–1 mm displacement)
→ Heartbeats (~1–3 Hz, ~0.1–0.5 mm)
→ Involuntary twitches
🔑 Core Insight Even a perfectly still animal cannot hide — breathing and heartbeat produce detectable phase modulation in the radar return. This is a physiological inevitability for all living vertebrates.
Technology | Detects Life? | Penetrates Bags? | 3D Imaging? | Ionizing Radiation? | Throughput
X-ray | No | Yes | No (2D only) | Yes | High
Thermal IR | Indirectly (heat) | No (blocked) | No | No | Medium
mmWave Radar | Yes (Doppler) | Yes | Yes (MIMO) | No | High
Manual Inspection | Yes | Yes (opening) | N/A | No | Low

## Slide 4
Radar Sensor Candidates
Four sensor options evaluated
4 / 16
TI IWR6843ISK
60 GHz | 3TX/4RX 12 virtual antennas Vital sign demo built-in ~$299–$799 USD
TI IWR1843BOOST
77 GHz | 3TX/4RX 12 virtual antennas On-chip DSP + MCU ~$349–$849 USD
TI IWRL6432BOOST
60 GHz | 2TX/3RX 6 virtual antennas Low power, compact ~$199–$699 USD
Infineon BGT60TR13C
60 GHz | 1TX/3RX 3 virtual channels 5.5 GHz bandwidth ~€250 EUR

## Slide 5
TI IWR6843ISK — 60 GHz mmWave Radar Sensor
Recommended starting point | ti.com/tool/IWR6843ISK
5 / 16
Feature | Specification
Frequency Band | 60–64 GHz
TX / RX Channels | 3 Transmitters, 4 Receivers (12 virtual antennas)
Bandwidth | Up to 4 GHz → range resolution ~3.75 cm
Detection Range | Up to 50 m (people); 0.3–2 m for vital signs
Velocity Resolution | ~0.1 mm/s Doppler micro-motion sensitivity
Field of View | ±60° Azimuth, ±60° Elevation
Output Interface | USB (via DCA1000EVM) or direct SPI
SDK / Processing | TI mmWave SDK, mmWave Studio, MATLAB/Python
Vital Sign Demo | Built-in: breathing rate & heartbeat rate detection
3D Imaging | Yes — MIMO virtual array + 3D point cloud + Doppler
Dimensions | 63.5 mm × 44.5 mm (standalone PCB)
Price | ~$299 USD (ISK) / ~$799 USD (with DCA1000EVM)
⭐ Most mature mmWave platform — TI provides ready-to-run lab demos for breathing/heartbeat detection. DCA1000EVM required for raw ADC data capture and custom 3D/Doppler processing.

## Slide 6
TI IWR1843BOOST — 77 GHz Industrial Radar Sensor
Higher frequency, on-chip processing | ti.com/tool/IWR1843BOOST
6 / 16
Feature | Specification
Frequency Band | 76–81 GHz
TX / RX Channels | 3 TX, 4 RX (12 virtual antennas)
Bandwidth | Up to 4 GHz → range resolution ~3.75 cm
Detection Range | Up to 100 m; 0.3–2 m for micro-motion
Velocity Resolution | Sub-mm/s Doppler sensitivity
Field of View | ±60° Azimuth, ±60° Elevation
On-Chip DSP | TI C674x DSP for real-time FFT & CFAR processing
On-Chip MCU | ARM Cortex-R4F for tracking & classification
3D Imaging | Yes — MIMO virtual array, 3D point cloud generation
Dimensions | 79 mm × 63.5 mm
Price | ~$349 USD (BOOST) / ~$849 USD (with DCA1000EVM)
🔧 Higher frequency (77 GHz) gives slightly better resolution + smaller antennas. On-chip DSP + MCU enables real-time embedded processing at the checkpoint — no external host required.

## Slide 7
TI IWRL6432BOOST — 57–64 GHz Low-Power Sensor
Compact & efficient | ti.com/tool/IWRL6432BOOST
7 / 16
Feature | Specification
Frequency Band | 57–64 GHz
TX / RX Channels | 2 TX, 3 RX (6 virtual antennas)
Bandwidth | Up to 4 GHz
Detection Range | Up to 20 m; 0.3–2 m for micro-motion
FOV | ±60° Azimuth, ±50° Elevation
Power | ~2.5 mW deep sleep / ~1.5 W active
Dimensions | 43 mm × 25 mm
Price | ~$199 USD (BOOST only)
✅ Advantages • Lowest power consumption • Smallest form factor • Best for battery-powered / space-constrained deployments • Lowest cost entry point
⚠️ Limitations • 2TX/3RX — only 6 virtual channels • Reduced 3D angular resolution vs. IWR6843/IWR1843 (12 virtual channels) • May not match 3D imaging quality

## Slide 8
Infineon DEMO BGT60TR13C — 60 GHz Radar Sensor
Compact sensor, high bandwidth | infineon.com
8 / 16
Feature | Specification
Frequency Band | 57–63 GHz (V-band)
TX / RX Channels | 1 TX, 3 RX (3 virtual channels)
Bandwidth | Up to 5.5 GHz → range resolution ~2.7 cm
Detection Range | Up to 15 m; 0.2–1 m for vital signs
FOV | ±45° Azimuth, ±45° Elevation
SDK | Infineon RDK, Radar Fusion GUI, Python SDK
Vital Sign Demo | Yes — dedicated vital sensing reference app
Sensor Size | 25 mm × 25 mm
Price | ~€250 EUR
✅ Advantages • Highest bandwidth (5.5 GHz) → finest range resolution (~2.7 cm) • Ultra-compact sensor (25×25 mm) • Can cascade multiple for custom MIMO
⚠️ Limitations • Single TX channel → no native MIMO imaging • Best for single-point vital sign detection, not full 3D imaging • Requires multiple synced boards for MIMO

## Slide 9
Radar Comparison Summary
Side-by-side sensor comparison
9 / 16
Sensor | Frequency | TX/RX | Max BW | 3D Imaging | Vital Sign Demo | Price (USD)
TI IWR6843ISK | 60 GHz | 3/4 (12 virt.) | 4 GHz | Yes (moderate) | Yes | $299–$799
TI IWR1843BOOST | 77 GHz | 3/4 (12 virt.) | 4 GHz | Yes (moderate) | Via custom DSP | $349–$849
TI IWRL6432BOOST | 60 GHz | 2/3 (6 virt.) | 4 GHz | Limited | Via custom DSP | $199–$699
Infineon BGT60TR13C | 60 GHz | 1/3 (3 virt.) | 5.5 GHz | No (single TX) | Yes | ~€250
🏆 Recommendation Start with TI IWR6843ISK — lowest barrier to entry, built-in vital sign demo, mature SDK, and proven 3D MIMO imaging capability at the lowest price point. For higher-resolution 3D imaging, consider cascading multiple IWR6843 units or IWR1843BOOST.

## Slide 10
Detection Mechanism — Warm-Blooded Animals
Birds & Mammals
10 / 16
Strong, rhythmic Doppler signatures from:
→ Breathing: 0.1–1 mm chest wall displacement, 0.1–3 Hz
→ Heartbeat: ~0.1–0.5 mm displacement, 1–3 Hz
Body temperature (~37°C) vs. ambient creates dielectric contrast
→ Enhances radar reflectivity at tissue boundaries
Detection Confidence: HIGH ✅
TI's vital-sign demos prove reliable extraction at 1–2 m
range through clothing and non-metallic barriers.
🫁 Breathing 0.1–1 mm 0.1–3 Hz ❤️ Heartbeat ~0.1–0.5 mm 1–3 Hz 🔥 Body Heat Dielectric Contrast

## Slide 11
Detection Mechanism — Cold-Blooded Animals
Reptiles & Amphibians
11 / 16
Weaker but present respiratory micro-motions:
→ Periodic throat / body wall movements
→ Lung ventilation at 0.05–0.5 Hz
Lower body temperature reduces dielectric contrast but:
→ Tissue structures (lungs, organs, skin) still reflect
Detection Confidence: MEDIUM–HIGH ⚠️
Dependent on animal size, activity level, and concealment.
Longer integration (5–15 s) increases SNR significantly.
🦎 Reptiles Throat / body movements 0.05–0.5 Hz 🐍 Amphibians Lung ventilation Periodic motion ⏱️ Longer Integration 5–15 seconds → Higher SNR

## Slide 12
Key Advantage Over Existing Technologies
Doppler = physiological inevitability
12 / 16
Unlike thermal cameras (which require the animal's body heat to reach the sensor with an unobstructed view) or X-ray (which sees only density), mmWave Doppler detection relies on physical motion — a physiological inevitability for all living vertebrates. Even at rest, breathing and heartbeat produce detectable phase modulation in the radar return. This cannot be masked by the animal — it is involuntary and continuous.
🌡️ Thermal IR
Blocked by fabric No 3D imaging Indirect detection only
☢️ X-ray
Ionizing radiation 2D only — no life detection Sees density, not motion
📡 mmWave Radar
Penetrates non-metallic 3D + Doppler detection Detects life itself

## Slide 13
System Architecture Concept
Clearance checkpoint deployment
13 / 16
Bag on Conveyor
▶
MIMO mmWave Radar Array (e.g. cascaded IWR6843)
▶
Real-Time Processor • Static 3D • Doppler • AI/ML
▶
Operator Display 🚦 Green/Amber/Red
Signal Processing Chain
1. Static 3D Reconstruction
FMCW range processing + MIMO angle estimation → volumetric voxel map
2. Doppler Micro-Motion Extraction
Coherent phase analysis Sub-mm displacements Physiological frequencies
3. AI/ML Fusion
Deep classifier on labeled radar signatures Shape + Doppler fusion
4. Alert Output
🟢 Green: Clear 🟠 Amber: Ambiguous 🔴 Red: Live animal

## Slide 14
Technical Risks & Mitigations
14 / 16
Risk | Mitigation
Low SNR for cold-blooded animals | Longer integration (5–15 s), higher-gain antenna arrays, matched filtering for respiratory waveforms
Metallic baggage lining (full reflection) | Secondary X-ray check + flag metallic contents — detection impossible through foil-lined bags
Conveyor motion clutter | Stationary radar geometry + Doppler clutter filtering removes constant-velocity belt motion
False positives (vibrating electronics, loose items) | Spectral pattern analysis + ML classifier to distinguish physiological (variable) from mechanical (single-frequency) motion
Throughput constraints | Fast FMCW chirp rates + parallel beamforming → < 5 s per bag dwell time

## Slide 15
Feasibility & Supporting Research
15 / 16
🏥 Remote Vital Sign Monitoring
Multiple peer-reviewed studies demonstrate mmWave detection of human heartbeat and respiration through clothing and blankets at 1–3 m (60–77 GHz FMCW). Same principles apply to animals. TI provides a production-ready vital signs demo with IWR6843.
🛂 Security Screening (Deployed)
MIMO mmWave body scanners for concealed object detection already deployed at airports (e.g., Rohde & Schwarz QPS systems at 70–80 GHz). Bag-screening adaptation is a straightforward extension.
🛟 Search & Rescue Life Detection
Lower-frequency Doppler radar is field-proven for detecting breathing survivors under rubble. mmWave brings higher spatial resolution appropriate for baggage-scale screening.

## Slide 16
Suggested Development Path
From benchtop to field deployment
16 / 16
Phase 1
Benchtop Validation
TI IWR6843ISK ($299) Built-in vital sign demo Test: respiration detection through fabric, plastic, cardboard at 0.5–2 m
▶
Phase 2
Custom MIMO Array
(If higher 3D resolution is required) Cascade multiple IWR6843 units or engage Vayyar
▶
Phase 3
ML Dataset Collection
Labeled recordings of: • Live animals • Inert objects • Various concealment scenarios
▶
Phase 4
Field Trial
Controlled checkpoint Measure: • Pd (detection probability) • Pfa (false alarm rate) Iterate & improve