## Slide 1
AMD FPGA Workflow for
AI Model Deployment on FPGA / SoC
Vitis AI • Vitis HLS • Vivado • Vitis — The AMD FPGA AI Pipeline
July 2026
1 / 13

## Slide 2
AMD FPGA AI Ecosystem — Four Core Tools
Target hardware: Zynq MPSoC / Zynq UltraScale+ / Versal ACAP
2 / 13
🧠 Vitis AI
AI-model quantization, compilation, and runtime (AI-specific pipeline)
⚙️ Vitis HLS
High-Level Synthesis C/C++ → RTL for custom operators DPU cannot handle
🔧 Vivado
Traditional FPGA design: RTL synthesis, place-and-route, IP integration, bitstream gen
💻 Vitis
Unified software platform: host app, PS–PL linking, platform creation, debug
💡 Zynq MPSoC / Versal ACAP combine ARM Processing System (PS) + FPGA Programmable Logic (PL) — DPU sits in PL while Linux + VART run on PS.

## Slide 3
Vitis AI Workflow — End-to-End Pipeline
From trained model to running DPU on FPGA
3 / 13
① Export
PyTorch / TensorFlow → ONNX
▸
② Quantize
Vitis AI Quantizer float32 → INT8
▸
③ Compile
Vitis AI Compiler → .xmodel
▸
④ Hardware
Vivado + Vitis DPU bitstream + platform
▸
⑤ Deploy
VART / Vitis AI Library Host App
PyTorch / TensorFlow (float32) │ ▼ ① Export to ONNX (or float model) │ ▼ ② Vitis AI Quantizer → INT8 model │ ▼ ③ Vitis AI Compiler → .xmodel file │ ▼ ④ Vivado + Vitis → DPU bitstream + platform │ ▼ ⑤ VART / Vitis AI Library → host application (C++ / Python)

## Slide 4
Step 1–2: Train, Export & Quantization
From float32 model to INT8 deployment-ready model
4 / 13
Step 1 — Train & Export
Train model in PyTorch or TensorFlow (float32)
Export to ONNX (Open Neural Network Exchange)
Or pass float model directly if framework natively supported
Vitis AI accepts ONNX + native TF/PyTorch formats
Step 2 — Quantization (Vitis AI Quantizer)
Convert weights & activations: float32 → INT8
Post-Training Quantization (PTQ) with small calibration dataset
100–1000 unlabeled samples → analyse activation distributions
If accuracy loss unacceptable: Quantization-Aware Training (QAT)
QAT tools: Brevitas (PyTorch) / QKeras / TF Model Optimization
Fine-tune model with simulated quantization during training
🔑 INT8 quantization reduces model size ~4× and enables efficient DPU execution with minimal accuracy drop for most CNN architectures.

## Slide 5
Step 3 — Vitis AI Compiler
Mapping the quantized model onto the DPU architecture
5 / 13
Feed quantized INT8 model into Vitis AI Compiler
Compiler maps model graph onto target DPU architecture
DPU configuration specified via arch.json file
Performs operator fusion optimizations:
→ BatchNorm folded into Convolution
→ Activation layers merged with preceding ops
Data-layout transformations for efficient DPU memory access
Instruction scheduling across DPU cores (multi-core support)
Output: .xmodel file — compiled instruction stream for DPU runtime
📦 Compiler Input / Output INPUT: • INT8 model (quantized) • arch.json (DPU config) OUTPUT: • .xmodel file The .xmodel contains: • DPU instructions • Weight data (INT8) • Graph execution plan • Multi-core scheduling
⚡ For most standard CNNs (ResNet, YOLO, MobileNet, VGG, etc.) the DPU handles all operators directly — no custom HLS accelerators needed.

## Slide 6
Step 4 — Hardware Platform (Vivado + Vitis)
Creating the FPGA bitstream with the DPU
6 / 13
🔧 Vivado — FPGA Hardware Design
Integrate DPU IP core into block design
Configure DPU: #cores, BRAM/URAM allocation, conv types
Add supporting IP: clocking, resets, AXI interconnects
Add sensor interfaces: MIPI/CSI camera receivers, etc.
Run synthesis → implementation (place-and-route)
Generate bitstream (.bit) + hardware hand-off (.xsa)
💻 Vitis — Platform Creation
Import .xsa from Vivado → create platform project
Packages hardware design with software stack:
→ FSBL (First Stage Boot Loader)
→ PMU firmware (Platform Management Unit)
→ Linux kernel + device tree
Enables host application ↔ DPU communication
Unified environment for system-level debug
⚙️ Vitis HLS (optional / advanced): For custom operators the DPU cannot natively support — write accelerator in C/C++, synthesize to RTL via Vitis HLS, integrate IP block alongside DPU in Vivado. Most standard CNNs do NOT need this.

## Slide 7
Step 5 — Deployment & Host Application
Flash bitstream + write host app with VART
7 / 13
Flashing the Bitstream
Method | Use Case
Vivado Hardware Manager (JTAG/USB) | Development / debugging
SD card / eMMC boot | Standalone embedded (Zynq MPSoC, Kria)
QSPI flash (program_flash) | Production, non-volatile boot
Ethernet / PCIe | Data-centre accelerator (Alveo)
Writing the Host Application — Vitis AI Runtime (VART)
C++ or Python API to load .xmodel and run inference
Submit inference jobs to DPU asynchronously
Vitis AI Library: higher-level wrappers with pre-built pipelines
Pre-processing: resize, normalize
Post-processing: NMS (object detection), softmax (classification)
Typical loop: capture → pre-process → DPU inference → post-process → act
┌──────────────────────────────────────┐ │ Processing System (ARM / Linux) │ │ ┌────────────────────────────────┐ │ │ │ Host App (C++ / Python) │ │ │ │ VART / Vitis AI Library │ │ │ └───────────┬────────────────────┘ │ │ │ AXI bus │ │ ┌───────────▼────────────────────┐ │ │ │ Programmable Logic (FPGA) │ │ │ │ ┌──────┐ ┌──────┐ ┌──────┐ │ │ │ │ │ DPU │ │ MIPI │ │Custom│ │ │ │ │ │ Core │ │ CSI │ │ HLS │ │ │ │ │ └──────┘ └──────┘ └──────┘ │ │ │ └────────────────────────────────┘ │ └──────────────────────────────────────┘

## Slide 8
Tool Summary — End-to-End Workflow
Complete tool chain from training to inference
8 / 13
Step | Tool | Input | Output
Train | PyTorch / TensorFlow | Dataset | float32 model
Export | torch.onnx / tf2onnx | float32 model | ONNX
Quantize | Vitis AI Quantizer | float32 model + calibration data | INT8 model
Compile | Vitis AI Compiler | INT8 model + arch.json | .xmodel
Hardware | Vivado | DPU IP + block design | bitstream (.bit) + .xsa
Platform | Vitis | .xsa | platform (boot, device tree)
Program | Vivado HW Manager / SD boot | bitstream | running DPU on FPGA
Host App | VART / Vitis AI Library | .xmodel + sensor data | inference results
🐳 Environment: Vitis AI tools ship as Docker containers (CPU & GPU variants). Vivado & Vitis are native Linux/Windows installs. DPU IP core is included with Vitis AI.

## Slide 9
External Resources & Learning Materials
Key references for FPGA-based AI deployment
9 / 13
🎓 Advanced FPGA Course: Verilog Based Robotics & Signal Processing
YouTube playlist — comprehensive FPGA course covering Verilog for robotics and DSP
🔗 https://www.youtube.com/playlist?list=PLfPwG72dAOx6gkqrrZVdr63EaizecO0Cg
🔬 hls4ml — Machine Learning to FPGA
Translate ML models directly into synthesizable VHDL or Verilog
🔗 https://fastmachinelearning.org/hls4ml/
🔥 PyTorch AI on FPGA — FINN Workflow Tutorial
Step-by-step tutorial for deploying PyTorch models on FPGA using the FINN framework
🔗 https://hugobrh.dev/posts/PY2FPGA/
🐍 Python to FPGA — Tutorial Snippets
Practical examples and code snippets for the Python→FPGA workflow
🔗 https://github.com/0BAB1/tutorial-snippets/tree/main/8%20Python%20to%20FPGA
🤖 Educational Platform for FPGA Accelerated AI in Robotics
Open-source platform demonstrating FPGA-accelerated AI for robotics applications
🔗 https://github.com/nhma20/FPGA_AI
📖 AMD Vitis AI 3.5 — Official Workflow Documentation
Official AMD documentation for the complete model deployment workflow
🔗 https://xilinx.github.io/Vitis-AI/3.5/html/docs/workflow-model-deployment.html

## Slide 10
AI Module Comparison — Edge Platforms (1/2)
NVIDIA Jetson, Hailo, and x86 edge platforms
10 / 13
NVIDIA Jetson AGX Orin
Up to 275 TOPS (INT8) 15W – 60W High-end robotics & autonomous navigation. Integrates CPU, Ampere GPU, and DLAs.
NVIDIA Jetson Orin Nano (Super)
Up to 67 TOPS (INT8) 7W – 25W Entry-level embedded AI & smart cameras. "Super" variant (Dec 2024) offers significant TOPS uplift over original.
Raspberry Pi 5 + Hailo-8 AI HAT
~13 to 26 TOPS 10W – 15W Low-power field robots. Hailo-8L = 13 TOPS Hailo-8 = 26 TOPS Separate Hailo accelerator.

## Slide 11
AI Module Comparison — Edge Platforms (2/2)
Intel x86 edge, Axelera, EdgeCortix, SiMa.ai
11 / 13
ASUS NUC 14
20–40+ TOPS (NPU+GPU) 28W – 65+W (system) Industrial edge / server. Full x86 + PCIe. Meteor Lake NPU ≈ 11 TOPS Arrow Lake NPU ≈ 13 TOPS Lunar Lake NPU ≈ 48 TOPS
Axelera AI Mini PC + M.2 Max
Up to 214 TOPS 20W – 40W In-memory computing (PIM) + RISC-V architecture. Ultra-low latency at high TOPS. Optimized for computer vision workloads.
EdgeCortix SAKURA
Up to 60 TOPS Under 10W FIM (Fabric in Memory) architecture. Targets low-power smart city & vision applications. Extremely efficient.
SiMa.ai MLSoC
Up to 50+ TOPS ~5–10W (board) Purpose-built for edge AI. Integrated CV/vision pipeline with software-programmable NPU. Power varies by workload.

## Slide 12
AI Module Comparison — Full Summary
Side-by-side comparison of all evaluated edge AI platforms
12 / 13
Platform / Device | Peak AI (TOPS) | Power | Primary Use Case & Architecture
NVIDIA Jetson AGX Orin | Up to 275 | 15W – 60W | High-end robotics, autonomous nav. CPU + Ampere GPU + DLA.
NVIDIA Jetson Orin Nano (Super) | Up to 67 | 7W – 25W | Entry-level embedded AI & smart cameras. Super variant (Dec 2024) uplift.
Raspberry Pi 5 + Hailo-8 AI HAT | 13 – 26 | 10W – 15W | Low-power field robots. Hailo-8L (13 TOPS) / Hailo-8 (26 TOPS) accelerator.
ASUS NUC 14 | 20 – 40+ | 28W – 65+W | Industrial edge / server. Full x86 + PCIe. Gen-dependent NPU performance.
Axelera AI Mini PC + M.2 Max | Up to 214 | 20W – 40W | In-memory computing (PIM) + RISC-V. Ultra-low latency at high TOPS.
EdgeCortix SAKURA | Up to 60 | Under 10W | FIM architecture. Low-power smart city & vision.
SiMa.ai MLSoC | Up to 50+ | ~5 – 10W | Purpose-built edge AI. Integrated CV pipeline + programmable NPU.

## Slide 13
Key Takeaways — AMD FPGA AI Deployment
Summary of the Vitis AI workflow
13 / 13
🧠 Complete Pipeline
AMD provides a full end-to-end tool chain: PyTorch/TF → ONNX → Quantize → Compile → Hardware → Deploy. Each step is handled by a dedicated tool in the ecosystem.
⚡ DPU Acceleration
The Deep Learning Processing Unit (DPU) is a hardened IP core optimized for CNN inference. INT8 quantization + operator fusion + multi-core scheduling deliver efficient FPGA acceleration.
🔧 Hardware Flexibility
Vivado + Vitis HLS allow custom hardware accelerators for non-standard operators. The FPGA can be tailored to the exact model architecture — not limited to fixed silicon.
🐳 Docker-Based Tooling
Vitis AI tools run in Docker containers (CPU/GPU variants) for easy setup. Vivado & Vitis are native installs for synthesis and platform creation.
🌐 Rich Ecosystem
Multiple external resources: hls4ml, FINN, educational FPGA-AI platforms, and official AMD documentation. Active community and growing adoption in edge AI.